## Slide 1
www.acaciawater.com
March 22, 2022
GIS and Remote Sensing for overlay analysis
Training Day 1 (AM)
/ Introduction to overlay analysis & QGIS
Dr. Maarten Waterloo

## Slide 2: Training program
Day | Program of activities (AM/PM)
Day 1 Tue., March 22nd | Introduction to overlay analysis & QGIS / Input data processing (lithology, land use)
Day 2 Wed., March 23rd | Input data processing (recharge, TWI) / Input data processing (lineament proximity & density)
Day 3 Thu., March 24th | Suitability map generation / Automation of suitability mapping
Day 4 Fri., March 25th | Suitability map styling / Introduction to Google Earth Engine
Day 5 Sat., March 26th | Introduction to Python

## Slide 3: Detailed program – Day 1
Time | Activities
9:00 – 12:00 | Introduction to GIS
 | Introduction to overlay analysis
 | Introduction to QGIS
12:00 – 13:00 | LUNCH BREAK
13:00 – 14:20 | Input layer – Lithology
15:40 – 16:00 | Input layer – Land use

## Slide 4: PART 1
Introduction to GIS

## Slide 5: What is GIS?
Geographical Information System

## Slide 6: Introducing GIS
Collection, storage, management and analysis of spatial environmental, demographic, and topographic data
 Valuable insights and revealing visualizations
 Help to make informed decisions
 Various applications
For additional information:
https://docs.qgis.org/3.16/en/docs/gentle_gis_introduction/index.html#gentle-introduction-gis

## Slide 7: GIS applications (1/4)
Mapping
e.g. Google Maps (navigation purposes)

## Slide 8: GIS applications (2/4)
Urban planning
e.g. designing and mapping of infrastructures and services, planning of urban growth
Notes: https://www.mdpi.com/2073-445X/10/1/85/htm

## Slide 9: GIS applications (3/4)
Disaster response
e.g. mapping of floods, wildfires, etc.
Notes: https://refubium.fu-berlin.de/bitstream/handle/fub188/19048/Belayneh-Application_of_GIS_and_Remote_Sensing_Techniques-244_001-Copy.pdf?sequence=1&isAllowed=y

## Slide 10: GIS applications (4/4)
Agricultural value chain
e.g. analysis of soil data, yield predictions, assisting precision farming, etc.
Natural resource management
e.g. biodiversity hotspots, allocation and distribution of water and forests, etc.

## Slide 11: GIS data – Vector vs Raster

## Slide 12: Spatial data acquisition
Direct acquisition (primary data)
  Ground-based field survey data
  Remotely sensed data from satellites, aircrafts or drones
Existing spatial data (secondary data)
  Printed maps
  Digitized data sets
  Processed data from firms or international agencies
Notes: Geological map boundaries  georeferencing (?)

## Slide 13: Spatial data acquisition – Georeferencing

## Slide 14: Spatial data acquisition – Satellite imagery & RS data
Landsat 9 OLI (Lake Tana, Oct 30th, 2021, to Feb 25th, 2022)
Landsat scenes
Landsat imagery
Landsat pixel (30x30 m)

## Slide 15: Spatial data acquisition – Satellite imagery & RS data
From satellite imagery to thematic maps
Landsat imagery
Classification
Thematic map

## Slide 16: Vector data
Lines
Points
Polygons

## Slide 17: Vector data – Attribute table
Lines
Points
Polygons
ID | Population | Region | Name
1 | 10346 | East | 
2 | 4503 | North | 
3 | 15950 | South | 

## Slide 18: Vector data – Time series

## Slide 19: Raster data
Columns
Rows
Width
Height

## Slide 20: Raster data – Digital Elevation Model (DEM)
A representation of the bare ground (bare earth) topographic surface of the Earth, excluding trees, buildings, and any other surface objects

## Slide 21: PART 2
Introduction to overlay analysis

## Slide 22: Overlay analysis – Principle
Vector
Vector
Vector
Raster
Raster
Raster

## Slide 23: Questions
What would be important spatial information to determine where to develop a waste dump?
And for groundwater suitability mapping?

## Slide 24: Overlay analysis – GW suitability mapping
Inform decisions on siting of GW wells,
Combined with other socio-economic and environmental factors
Input layers
  Lithology
  Recharge
  Land use
  Slope / TWI (Topographic Wetness Index)
  Lineament density
  Lineament proximity
Notes: Slope OR Topographic Wetness Index?

## Slide 25: Overlay analysis - Workflow
STEP 0: Data acquisition and basic processing
STEP 1: Pre-processing
  > Clip, resample, reproject, classify, calculate
STEP 2: Overlaying
  > Classes and scores, weights, average suitability
STEP 3: Sensitivity analysis

## Slide 26: Overlay analysis - Result

## Slide 27: Part 3
Introduction to QGIS

## Slide 28: Why QGIS?
Powerful GIS used to process, analyse and display geographic information
100% Free and Open-source (FOSS)
Intuitive interface and customizable
Wide range of data and functionnalities
Active community of users (Esri, GISuser, GIS Lounge)
Free Qfield for offline use on tablets and phones
Notes: For additional information:
https://docs.qgis.org/3.16/en/docs/training_manual/index.html

## Slide 29: QGIS main functionnalities
Mapping
Data management
Geoprocessing

## Slide 30: QGIS – Install software
QGIS Standalone Installer Version 3.22
Install from USB stick
OR
Download the QGIS installer at:
https://qgis.org/downloads/QGIS-OSGeo4W-3.22.4-1.msi

## Slide 31: QGIS – Plugins
Many new features and functions can be easily added to the application
Written in Python
Execution of specific tasks
Useful plugins:
  SRTM-Downloader, for elevation data
  QSWAT3, for watershed hydrological modeling
  GEE (Google Earth Engine)
Install from Plugins > Management, and > Install plugins
Notes: For information

## Slide 32: QGIS – Create a basic map (/)
Open a new GIS project
Directories
CRS

## Slide 33: Projections

## Slide 34: Overview of the interface
Notes: Include caption

## Slide 35: QGIS – Create a basic map (/)
Download input data
Searching for data
Data sources: Google Earth Engine, etc.
Key words on internet: using ‘dataset’ ‘data’ ‘database’ on ‘blabla’

## Slide 36: QGIS – Create a basic map (/)
Adding vector layer
Attribute table
Symbology

## Slide 37: QGIS – Create a basic map (/)
Adding raster layer
Symbology

## Slide 38: QGIS – Layer styling

## Slide 39: QGIS – Webservices
Data sources online from which you can load data as long as you are connected to the Internet
Web Mapping Services (WMS), a service hosted on a remote server which provides maps
Web Feature Services (WFS), which provides GIS data in formats that can be loaded directly in QGIS and edited
Relative to groundwater database platform:
https://mowe.acaciadata.com/
Notes: For information
What servers done? How are they built? Check projects on QGIS

## Slide 40
March 22, 2022
Thank you for your attention
van Hogendorpplein 4, 2805 BM Gouda, the Netherlands
telephone: +31 (0)182 - 686 424
info@acaciawater.com | www.acaciawater.com