## Slide 1
www.acaciawater.com
March 22, 2022
GIS and Remote Sensing for overlay analysis
Training Day 1
PM / Input data processing (1/3)
Dr. Maarten Waterloo

## Slide 2: Training program
Day | Program of activities (AM/PM)
Day 1 Tue., March 22nd | Introduction to overlay analysis & QGIS / Input data processing (lithology, land use)
Day 2 Wed., March 23rd | Input data processing (recharge, TWI) / Input data processing (lineament proximity & density)
Day 3 Thu., March 24th | Suitability map generation / Automation of suitability mapping
Day 4 Fri., March 25th | Suitability map styling / Introduction to Google Earth Engine
Day 5 Sat., March 26th | Introduction to Python

## Slide 3: Detailed program – Day 1
Time | Activities
9:00 – 12:00 | Introduction to GIS
 | Introduction to overlay analysis
 | Introduction to QGIS
12:00 – 13:00 | LUNCH BREAK
13:00 – 16:00 | Overlay analysis – Step 1
 | Input layer – Lithology
 | Input layer – Land use

## Slide 4: Overlay analysis - Workflow
STEP 0: Data acquisition and basic processing
STEP 1: Pre-processing
  > Clip, resample, reproject, classify, calculate
STEP 2: Overlaying
  > Classes and scores, weights, average suitability
STEP 3: Sensitivity analysis

## Slide 5: Part 1
Introduction of Overlay Analysis – Step 1

## Slide 6: Step 1 – Principle
Output:
  Overlay layers with uniform resolution, extent and CRS: lithology, land use, recharge, slope, lineaments (x2)
Input:
  CRS (WSG84, UTM 37N), resolution (100 m)
  Input maps: extent, lithology, DEM, land use, lineaments (x2), precipitation, evapotranspiration
  Look-up tables (lithology and land use classes)
  Style definitions

## Slide 7: Step 1 – Input data
Primary data:
  Lithology
  Recharge
  Land use
  Slope/Topographic Wetness Index (TWI)
  Lineaments
Secondary data:
  Evapotranspiration
  Vegetation Index
  Soil moisture
  Hydrology (catchments, drainage network, wetness index)

## Slide 8: Step 1 – Main geo-algorithms
Clipping to cluster extent
Reprojection and resampling (average or mode) to desired resolution
Calculation (recharge, slope, density, proximity)
Classification (lithology, land use)

## Slide 9: Geo-algorithms – Clipping

## Slide 10: Geo-algorithms – Reproject

## Slide 11: Geo-algorithms – Resample

## Slide 12: Geo-algorithms – Join
+
=
Shapefile
Excel/csv/txt
Infiltration coefficient

## Slide 13: Geoalgorithms – Rasterize

## Slide 14: Geo-algorithms – Calculation
Field calculator
Raster calculator
Graphical modeler

## Slide 15: Geo-algorithms – Reclassify

## Slide 16: Part 2
Pre-processing of lithology layer

## Slide 17: Pre-processing – Lithology layer
Source: Harmonized geological map
Classification: from 104 => to 7 classes
Class | Description
1 | Loose quaternary sediments, including elluvials and Miocene sediments
2 | Rift pyroclastics and rift silicics
3 | Upper basalts + Quaternary highland basalts + Rift basalts
4 | Lower basalts
5 | Limestone + Upper sandstone + Shale + Marl + all other Mesozoics
6 | Low grade basement and Adigrate sandstone
7 | High grade basement

## Slide 18: Lithology layer – Procedure
Load woreda extent (vector)
Load harmonized geological map (vector)
Load lithology classes (delimited text)
Join table with classes to map using “code” column
  > Double click on layer name, then go to Joins menu
If joined field is a string (aligned left), then change to number (aligned right) > Field calculator
Reproject map to UTM37N, WGS84 (EPSG:32637) > Warp
Rasterize reprojected map using 7 classes, set resolution to 100m and extent to woreda extent > Rasterize

## Slide 19: Lithology layer – Classification
Harmonized geological map
7 lithology classes

## Slide 20: Part 3
Pre-processing of land use layer

## Slide 21: Pre-processing – Land use
Source: 2016 Sentinel-2A imagery (20 m)
Reclassification into 5 classes
Class | Description
1 | Cropland
2 | Bush and rangeland
3 | Forest
4 | Bare soil and degraded land
5 | Urban area

## Slide 22: Land use layer – Procedure
Load extent (vector)
Load land use data (raster)
Reclassify landuse to 5 classes > r.reclass, using overlay/classes/landuse_esa.txt
Reproject and resample landuse to UTM37N, WGS84 with resolution 100m and clip to extent (think about resampling method to use) > Warp (Hint: use ‘Mode’ for resampling methods)

## Slide 23: Land use layer – Reclassification
Land use ESA (20 m)
Reclassified land use (100 m)

## Slide 24
February 26, 2019
Thank you for your attention
van Hogendorpplein 4, 2805 BM Gouda, the Netherlands
telephone: +31 (0)182 - 686 424
info@acaciawater.com | www.acaciawater.com